## Slide 1: ESS 411/511 Geophysical Continuum Mechanics Class #4
Highlights from Class #3 – Alysa Fintel
Today’s highlights on Friday – Anna Ledeczi
Warm-up question (break-out) –
What is a creep function?
What is a relaxation function?

## Slide 2: Announcements
When I set up the sign-up schedule for class highlights, I hadn't properly accounted for the November 11 Veteran's Day holiday. It should be correct now. If you had signed up to highlight a class around Nov 11 or later, please check that the revised schedule still works for you. Thanks.
On the Canvas home page, I have added
a link to a calendar showing daily topics
links to FILES folders where you can find the slides from past lectures, and your Highlights reports from those lectures.
Homework #1 is live on Canvas. Please check it out and bring questions to our HW Lab on Thursday.

## Slide 3: ESS 411/511 Geophysical Continuum Mechanics Class #3
Broad Outline for the Quarter
Continuum mechanics in 1-D
1-D models with springs, dashpots, sliding blocks
Mathematical tools – vectors, tensors, coordinate changes
Stress – principal values, Mohr’s circles for 3-D stress
Coulomb failure, pore pressure, crustal strength
Measuring stress in the Earth
Strain – Finite strain; infinitesimal strains
Moments – lithosphere bending; Earthquake moment magnitude
Conservation laws
Constitutive relations for elastic and viscous materials
Elastic waves; kinematic waves

## Slide 4: ESS 411/511 Geophysical Continuum Mechanics Class #4
Class-prep answers (break-out)
This was the assignment:
Energy and dissipation If you manually compress a perfect spring and then release it back to its initial state (a strain cycle), no energy gets converted into heat, but if you manually drive a perfect dash-pot through a similar strain cycle, some energy is always converted to heat.
Without resorting to any equations, explain to a nonscientific family member why this has to be true, based your efforts expended in the two experiments.
Share with partners your explanations of energy dissipation (or not) in cyclical springs and dash-pots.

## Slide 5: ESS 411/511 Geophysical Continuum Mechanics Class #4
For Friday (class #5)
Please review the section in Raymond Ch 2, Section 2.9 on harmonic loading, and start reading Mase, Smelser, and Mase, Ch.2, through Section 2.3.
When a viscoelastic material is loaded harmonically at a frequency w, the attenuation (Q-1) of that sinusoidal signal depends on the relation between w and a characteristic time t of the material.
With reference to the Standard Linear Solid model, please explain in words why energy loss (attenuation Q-1) is minimal at high and low frequencies, but is high at mid-range.
Your class-prep assignment on frequency-dependent attenuation

## Slide 6: ESS 411/511 Geophysical Continuum Mechanics Class #3
A model for idealized real materials
.
Forces are balanced
Each element feels the same force F
-F
F

## Slide 7: Rheological tests
Creep tests
Apply a constant stress s
e.g. put a weight on top of a sample
Measure strain e(t) or strain rate
Constant strain-rate tests
Apply a constant strain rate
e.g. with a motor-driven vice
Measure stress s(t)
Relaxation tests
Apply an abrupt strain e, then hold it constant
e.g. abrupt shortening in a vice.
Measure stress s(t) as sample adjusts.

## Slide 8: Models for linear solids
Those springs and dashpots …

## Slide 9: Viscoelastic model
m1
Elastic
Delayed Elastic
Viscous
m2
Called Maxwell Solid, if h1 = ∞, m1 = ∞
Called Kelvin-Voigt Solid, if h2 = ∞, m2 = ∞
Called Standard Linear Solid, if h2 = ∞

## Slide 10: Creep Test with Viscoelastic model

## Slide 11: Viscoelastic behavior in real materials
Changes in the microstructure at the crystal level inside the sample can alter the effective viscosity after significant strain as the test progresses.
e.g. crystal basal planes align for easy glide
microcracks may develop, allowing internal slip
e
Stress
Strain

## Slide 12: Maxwell solid
m
time
s
e
?
Also Homework set #1
Is there a characteristic time for the material?
h/m ?

## Slide 13: Kelvin-Voigt solid
m
time
s
e
?
Is there a characteristic time for the material?
h/m ?
Notes: Project onto white board, invite students to sketch response

## Slide 14
A shock absorber can be modeled as a delayed elasticity Kelvin-Voigt solid.
m

## Slide 15: Kelvin-Voigt Response
At t = 0, spring hasn’t shortened; dashpot supports all the stress s , so
e(0) = 0 (*)
At t = ∞, dashpot has stopped; spring supports all the stress s, so
e(∞) = s/m (**)
The transition is probably a decaying exponential. (Let’s try it …)
t=h/m must be the time constant defining the transition.
m
Spring and dashpot together support stress s
With the boundary conditions (*) and (**), A can be found, and solution is …

## Slide 16: Response to constant loading s
Elastic
Delayed Elastic
Viscous
m2
m1
Generalized linear viscoelastic solid

## Slide 17: How did we get that?!
Elastic
Delayed Elastic
Viscous
m2
m1
Each element feels the same stress s,
We just added up the strains in each element

## Slide 18: The Raymond notes also give creep functions and relaxation functions for step changes in stress or strain
C(t-t’) is the creep function
Creep test
=
Applied stress s
k(t-t’) is the relaxation function
Relaxation test
e
e
=
k
k
s
Applied strain s

## Slide 19: Relaxation Function in Standard Linear Solid (h2 = ∞)
At t=0 :
The spring m1 in the K-V element is prevented from deforming, due to h1.
All applied strain e is taken up initially in the spring m2. So s(0) =m2e
(Do you agree that (*) shows this?)
Stress s(0) also acts on the K-V element, so it also begins to strain.
(
)
(*)
m2
m1
X
e = constant (after t=0)
For a K-V element, (strain e(0) = 0 ✓).
At t=0, the strain rate in the K-V element is
By differentiating with respect to time t,
m = m1
h = h1

## Slide 20: Relaxation Function in Standard Linear Solid (h2 = ∞)
At t > 0
The K-V element is starting to strain at the rate ,
(
)
(*)
m2
m1
X
e = constant
K-V begins to take over some of the strain from the spring m2.
Strain e1 increases in spring m1 and h1, and strain e2 decreases in spring m2
e1 + e2 = e
Because strain is decreasing in spring m2, stress s(t) must be decreasing.
Strain e1 in spring m1 cannot exceed s∞/m1
Dash-pot h1 must eventually stop moving.
This means there is no stress in the dash-pot at t=t∞
There will be a time constant t
that depends on m2, m1 and h1

## Slide 21: Relaxation Function in Standard Linear Solid (h2 = ∞)
At t = ∞
(
)
(*)
m2
m1
X
e = constant
Strain e1 in spring m1 cannot exceed s∞/m1
Dash-pot h1 must eventually stop moving.
This means there is no stress in the dash-pot at t=t∞
Both springs m1 and m2 then support the same stress s∞, so
or
is the limiting stress at t=t∞

## Slide 22: Relaxation Function in Standard Linear Solid (h2 = ∞)
(
)
(*)
m2
m1
X
e = constant
Strain e
Stress s(t)/e
m2
Time t
0

## Slide 23: Energy and Work
In Continuum – work done per unit volume:
= stress × strain
= stress × strain rate
Rate of doing work per unit volume
(overdots indicate time derivatives)
Work W is force F acting through a distance d
Work for point particles: W = F d

## Slide 24: Energy and Work
For elastic material, substitute: s(t) = me(t)
DE(t) returns to zero whenever s returns to zero.
All energy is recovered
Total energy input between from time 0 to t

## Slide 25: Energy and Work
Total energy input between from time 0 to t
For viscous material:
The integrand is always positive.
DE(t) can never return to zero if strain rate is ever nonzero
energy is always lost if any strain has occurred.